## Slide 1: Current State - No control
Region 4 reaches ≈ 110 veh/km → flow collapses  “Gridlock”
Average journey time > 1 h.
Long waiting time: 45 min
No anticipation of future traffic
Traffic flow with no control leads to gridlock, marked in red.

## Slide 2: Failure mode - P controller
P-controller reduces journey time by 20% yet can’t handle late‑rush surge.
Single‑region feedback ignores upstream queues.
Same speed factor broadcast to all five roads → sub‑optimal.
A drastic reduction in CO2 emissions and travel time can be achieved with a new controller
Traffic flow with P-control still leads to gridlock, marked in red.

## Slide 3: MPC Model Predictive Control
Predictable behaviour
Easy to follow DSL changes
Can anticipate future traffic
Avg travel time −72.5 % • 100 % trips completed
Traffic flows freely without gridlock using the MPC controller

## Slide 4: TPC Transient Predictive Control
Can deal with closed loop training data
Fast compilation time
Fastest average travel time
Avg travel time −80 % • Solves ≈ 3× faster than MPC
Traffic flows freely without gridlock using the TPC controller
TPC makes accurate density predictions
Density [# vehicles/km]

## Slide 5: Deployment
Implementation
Phase | Model-based MPC | Data-driven TPC
1. Offline preparation | Identify real world model and linearize around operating point | Collect 1-2 weeks of DSL commands, densities and flows from the real network (excite each road a bit to cover the dynamics).
2. Implementation | Implement hardware to run the controller Include a Kalman or moving-average state estimator to filter sensor noise. | Implement hardware to run the controller No explicit state estimator—uses raw measured inputs/outputs.
3. Monitoring & updates | Re-identify model yearly or after major roadworks Retune parameters if traffic patterns shift. | Retrain predictors monthly with the newest data. No manual gain retuning needed in most cases.
Trade-offs
Aspect | Model-based MPC | Data-driven TPC
Up-front effort | Needs a trustworthy physics-based model and calibration → more engineering hours. | Minimal modelling; biggest cost is gathering representative data.
Transparency & verification | High: linear model + quadratic cost allow formal proofs of stability and constraint satisfaction. | Medium‑high: predictors are linear and inspectable but still data‑driven.
Adaptability to network changes | Requires revisiting the model and gains after structural changes. | Simply collect new data and retrain; quick to port to other corridors.
Robustness to unseen scenarios | Good if the model covers the operating envelope; brittle outside it. | Same risk as any data‑driven method: edge-case behaviour may be unknown

## Slide 6: Bonus: DeePC Data-enabled Predictive Control
Better at capturing complex behaviour
Uses real SUMO data—no model mismatch.
More complex DSL changes
More parameters to tune, requiring extra expertise
Avg travel time −74 % • Solves ≈ 2× faster than MPC
Traffic flows freely without gridlock using the DeePC controller
DSL changes may be more challenging for human drivers.